Assignment No: 8
Adjustment of Horizontal Surveys:
Traverses and Networks

Objectives: To learn and gain experience with adjustment of traverses and networks.

1) Adjust the network shown below by the method of least squares. (10 pts.)

Course	Distance (m)	
BC	1320.027	0.023
CD	1579.169	0.023
DA	1664.497	0.023
AC	2105.995	0.023
AB	1640.033	0.023

	Angle	
BAC	38º48’52.5”	2.2”
CBA	90º02’25.5”	3.1”
DCA	51º18’21.9”	2.3”
CAD	47º46’13.1”	2.3”
ACB	51º08’53.2”	2.6”

The coordinates (m) for control station A is x = 4356.78, y = 2340.97. The azimuth of line AB is AzAB=0º 06’ 23.7” with a standard deviation of 1”.

a) What is the reference standard deviation, S0?

b) List the adjusted coordinates of the unknown stations and their standard deviations.

c) Tabulate the adjusted observations, their residuals and their standard deviations.

d) Compare your results with the ones which you obtained both in the Assignment-VI and in the Assignment-VII and comment on them.